## Slide 1: RGB Plot Profile
A plugin for Fiji
Microscopic Imaging Center

## Slide 2: RGB Plot Profile plugin
Plot profile is a useful Fiji function in which a two-dimensional graph is made of the intesity values of all the pixels that lie along a ROI line or rectangle selection; however, the plot profile only works for grayscale images.
The RGB Plot Profile plugin is a quick way to achieve the same results for an RGB type image or an equivalent three channel image.
It produces a plot for every colour separately along the same ROI and combines the plots into a single graph which clearly shows the different plots by colour.

## Slide 3
RGB image with a line selection (in yellow)
Plot profile of all three channels identified by their colour
The plugin pipeline

## Slide 4: Requirements
The RGB Plot Profile plugin requires either an RGB image or a multichannel image with (at least) three channels.
Please note that the channels of the multi-channel image can be any type of signal and do not need to be red, green and blue. If more than three channels are available, the first three will be used for the profile.
The plugin will run on image stacks with multiple slices and/or time frames, but it will only plot the current slice/frame.
It is also possible to run the plugin on a multi-slice or –frame image with less than three channels, in which case the first three slices/frames will be used instead (slices will be used before frames).

## Slide 5: User parameters
Selection:
  The RGB Plot Profile plugin uses either a line or a rectangular selection as the base for its plot.
  For the line selection, a straight, segmented, and freehand line are all acceptable. The plot will be made for all pixels along the selection and the distance in the plot is also the distance along the line at which the pixel is positioned.
  For the rectangular selection, the plot is always taken along the x-axis and is an average of all pixel values within the selection with the same x-coordinate. Note that for rectangular selections, the rounded and rotated rectangle options are not supported.

## Slide 6: Adaptation options
There are no specific adaption options for this plugin.

## Slide 7: Installation
Copy the plugin to the ‘plugins/Macros’ folder in your Fiji.app installation folder.

## Slide 8: User manual
Make sure that you have the RGB or 3 channel composite image that you want to use as the active image in Fiji.
Select one of the line selection tools or the rectangle tool in the Fiji toolbar and draw the plot line on the image.
Activate the plugin in Plugins > Macros.
The profile plots of the three colours will be shown in the same, new RGB image.